## Slide 1: CAN Interface for Automation of the Dyno Bench
Michele IMBARRATO
SRA LAB

## Slide 2: Index of topics
AGENDA
01
Objective of the work
02
Validation of the existing CAN library
03
Implemented changes and developments
04
Advanced validation and debugging
05
DBC file: structure and updates
06
Vector CANalyzer and GUI integration
07
Conclusions and results

## Slide 3: Objective of the work
OBJECTIVE
The aim of the project is to develop a CAN interface to automate the communication between the microcontroller (uC) and the Dyno bench software.
1
Library validation
Verifying and Correcting the Existing SR5E1 CAN Library.
2
Edit DBC file
Modification of the DBC file by adding new CAN messages.
3
Creation of control GUI
Development of the control and monitoring graphical interface (GUI).

## Slide 4: Validation of existing CAN library

## Slide 5: Architecture and offset rule
CAN LIBRARY
The initial library was designed to interface the test bench (Dyno bench) with the firmware of the Stellar-E microcontroller via CAN bus. It adopts the Dyno-to-Dishwasher (DYNO2DW) protocol: a translation function that converts the CAN commands of the bench into the format of the ST Motor Control Dishwasher protocol.
Dyno Bench
DYNO2DW
(translation)
Firmware Stellar-E
(ST MC Protocol)
+0x30 Offset
Input commands from the Dyno bench to the inverter.
+0x40 Offset
Outgoing Diagnostics to the Dyno bench.

## Slide 6: Periodic diagnostics— Send_Status
To allow the Dyno bench to monitor the status of the inverter in real time, the library integrates a periodic diagnostic function that sends a stack of messages every 100 ms.
10
Diagnostic Registers
100 ms
Sending interval
It iterates over the 10 registers and reads their current value
Packages the data in the CAN frame buffer
Triggers transmission via dedicated IRQ handler
#define CAN_NUM_MSG 10
uint8_t msg_tx_diag_can[CAN_NUM_MSG] = {
MC_PROTOCOL_REG_UNDEFINED, // counter, update 100ms
MC_PROTOCOL_REG_SPEED_REF,
MC_PROTOCOL_REG_TORQUE_REF,
MC_PROTOCOL_REG_FLUX_REF,
MC_PROTOCOL_REG_BUS_VOLTAGE,
MC_PROTOCOL_REG_HEATS_TEMP,
MC_PROTOCOL_REG_SPEED_MEAS,
MC_PROTOCOL_REG_TORQUE_MEAS,
MC_PROTOCOL_REG_STATUS
};
uint8_t Send_Status(MCP_Handle_t *pHandle) {
if (FCP_TRANSFER_IDLE == pHandle->pFCP->TxFrameState) {
for (i = 0; i < CAN_NUM_MSG; i++) {
support_buffer = UI_GetReg(&pHandle->_Super, Register, NULL);
}
pHandle->pFCP->TxFrame.Code = code;
pHandle->pFCP->TxFrame.Size = size;
DBCCAN_TX_IRQ_Handler(pHandle->pFCP);
}
}
MC_PROTOCOL_REG_FLUX_MEAS,
CAN LIBRARY

## Slide 7: Transmission and Reception Mechanisms
Transmission
Send_Status Function
1
Reads register value with UI_GetReg()
2
Formats the 4 data bytes in little-endian
3
Assigns the converted ID with a +0x40 offset
4
Calls DBCCAN_TX_IRQ_Handler to transmit via FDCAN
Reception
DYNO2DWProtocol function (from ISR IRQ_CAN1_LINE0_HANDLER)
1
Analyzes command code (EXECUTE_COMMAND, SET_RAMP, etc.)
2
Reconstructs the packet in the ST format (Code, Length, Payload)
3
Calculates checksum with SelfCRCCalc(msg)
4
Passes bytes to CFCP_RX_IRQ_Handler, managing timeout timers
CAN LIBRARY

## Slide 8: CAN Command Mapping
Incoming Commands — Offset 0x30
Outgoing diagnostics— Offset +0x40
ID | Command | Description
0x33 | EXECUTE_COMMAND | Status Controls: Motor Start/Stop, Reset, Alignment
0x37 | SET_RAMP | Speed Ramp configuration (Value and Duration)
0x31 / 0x32 | SET_REG / GET_REG | Register Write and Read
0x3A | SET_CURRENT_ID_IQ | Simultaneous setting of Id and Iq values
0x3F / 0x41 | SET_CURRENT_ID / SET_CURRENT_IQ | Independent setting of Id and Iq values
0x3E / 0x3F | SET_ID_RAMP / SET_IQ_RAMP | Current ramps configuration (Value and Duration)
ID | Command | Description
0x42 | DIAG_STATE_MC | Machine status
0x5A | DIAG_TEMPERATURE | Temperature
0x59 | DIAG_BUS_VOLTAGE_MEAS | BUS voltage
0x60 / 0x4C | DIAG_FLUX_MEAS / DIAG_FLUX_REF | Measured and reference Id
0x5F / 0x48 | DIAG_TORQUE_MEAS / DIAG_TORQUE_REF | Measured and reference Iq
0x5E / 0x44 | DIAG_SPEED_MEAS / DIAG_SPEED_REF | Measured and reference Speed
CAN LIBRARY

## Slide 9: Implemented Changes and Developments

## Slide 10: Command Handling Refactoring
State command execution (EXECUTE_COMMAND) was redesigned to eliminate redundancies and multiple sends on the bus.
✕
BEFORE
Chain of separate if statements: potential multiple and redundant transmissions on the bus. Each EXECUTE_COMMAND message could attempt to set the machine to both START and STOP.
✓
AFTER
Mutually exclusive execution (if – else if): only one valid command at a time, with unambiguous resolution of machine START and STOP.
Flags Evaluated by the System
The system evaluates the flags received from the bank and sets the MC_PROTOCOL_CMD_* code corresponding to the selected command.
validCommand = true
set for only one flag at a time
DEVELOPMENTS

## Slide 11: Code comparison — EXECUTE_COMMAND
BEFORE
AFTER
case EXECUTE_COMMAND:
bool validCommand = true;
msg[0] = MC_PROTOCOL_CODE_EXECUTE_CMD;
msg[1] = 0x1;
if (RxArr[0] & EXE_START_MOTOR) {
msg[2] = MC_PROTOCOL_CMD_START_MOTOR;
}
else if (!(RxArr[0] & EXE_START_MOTOR)) {
msg[2] = MC_PROTOCOL_CMD_STOP_MOTOR;
}
...
else {
validCommand = false;
}
if (validCommand) {
msg[3] = SelfCRCCalc(msg);
for (count = 0; count < (msg[1]+3); count++) {
*retV = *(uint16_t*)(CFCP_RX_IRQ_Handler(
&pFDCAN, msg[count]));
}
}
case EXECUTE_COMMAND:
msg[0] = MC_PROTOCOL_CODE_EXECUTE_CMD;
msg[1] = 0x1;
if (RxArr[0] & EXE_START_MOTOR) {
msg[2] = MC_PROTOCOL_CMD_START_MOTOR;
msg[3] = SelfCRCCalc(msg);
}
else {
msg[2] = MC_PROTOCOL_CMD_STOP_MOTOR;
msg[3] = SelfCRCCalc(msg);
}
for (count = 0; count < (msg[1]+3); count++) {
*retV = *(uint16_t*)(CFCP_RX_IRQ_Handler(
&pFDCAN, msg[count]));
}
if (RxArr[0] & EXE_RESET) {
msg[2] = MC_PROTOCOL_CMD_RESET;
msg[3] = SelfCRCCalc(msg);
for (count = 0; count < (msg[1]+3); count++) {
*retV = *(uint16_t*)(CFCP_RX_IRQ_Handler(
&pFDCAN, msg[count]));
}
}
DEVELOPMENTS

## Slide 12: Independent control of I_d/I_q currents
Dedicated References
Dedicated commands MC_PROTOCOL_CODE_SET_CURRENT_ID_REF and MC_PROTOCOL_CODE_ SET_CURRENT_IQ_REF, using IDs not previously used in the library and their corresponding (+0x30) values on the DYNO side
Implementation of case statements in the DYNO2DW function, matching payload length to the number of bytes required by the function
16-bit signed decoding directly from CAN buffer bytes
Independent application using UI_SetIdRef() and UI_SetIqRef()
#define MC_PROTOCOL_CODE_SET_CURRENT_ID_REF 0x0F
#define MC_PROTOCOL_CODE_SET_CURRENT_IQ_REF 0x11
case SET_CURRENT_ID:
msg[0] = MC_PROTOCOL_CODE_SET_CURRENT_ID_REF;
msg[1] = 0x2;
case SET_CURRENT_IQ:
msg[0] = MC_PROTOCOL_CODE_SET_CURRENT_IQ_REF;
msg[1] = 0x2;
case MC_PROTOCOL_CODE_SET_CURRENT_ID_REF: {
int16_t hIdRef = (int16_t)buffer[0] +
((int16_t)buffer[1] << 8);
UI_SetIdRef(&pHandle->_Super, hIdRef);
bNoError = true;
} break;
case MC_PROTOCOL_CODE_SET_CURRENT_IQ_REF: {
int16_t hIqRef = (int16_t)buffer[0] +
((int16_t)buffer[1] << 8);
UI_SetIqRef(&pHandle->_Super, hIqRef);
bNoError = true;
} break;
DEVELOPMENTS

## Slide 13: I_q Ramp
Dedicated references
Command and function already present in the library
Implementation of case statements in the DYNO2DW function, with payload length equal to the number of bytes required by the function
case SET_IQ_RAMP:
msg[0] = MC_PROTOCOL_CODE_SET_TORQUE_RAMP;
msg[1] = 0x6;
...
case MC_PROTOCOL_CODE_SET_TORQUE_RAMP: {
uint16_t duration = buffer[4] +
(buffer[5] << 8);
int32_t torque = buffer[0] + (buffer[1] << 8) +
(buffer[2] << 16) + (buffer[3] << 24);
bNoError = UI_ExecTorqueRamp(
&pHandle->_Super, torque, duration);
} break;
DEVELOPMENTS

## Slide 14: I_d Ramp
Dedicated references
Dedicated commands MC_PROTOCOL_CODE_SET_FLUX_RAMP, using ID not yet in use in the library and their corresponding (+0x30) on the DYNO side
Implementation of case statements in the DYNO2DW function, matching payload length to the number of bytes required by the function
Implementation of UI_ExecFluxRamp, MCI_ExecFluxRamp, and STC_ExecFluxRamp functions
#define MC_PROTOCOL_CODE_SET_FLUX_RAMP
case SET_ID_RAMP:
msg[0] = MC_PROTOCOL_CODE_SET_FLUX_RAMP;
msg[1] = 0x6;
...
case MC_PROTOCOL_CODE_SET_FLUX_RAMP: {
qd_t hqd;
uint16_t duration = buffer[4] +
(buffer[5] << 8);
UI_Handle_t* Name = &pHandle->_Super;
MCI_Handle_t* Name2 =
Name->pMCI[Name->bSelectedDrive];
hqd = MCI_GetIqdref(Name2);
hqd.d = buffer[2] + (buffer[3] << 8);
bNoError = UI_ExecCurrentRamps(
&pHandle->_Super, hqd, duration);
} break;
DEVELOPMENTS

## Slide 15: I_d Ramp — Implementation
Call chain from the UI layer to ramp calculation in the State Machine Functions.
UI_ExecFluxRamp / MCI_ExecFluxRamp
__weak bool UI_ExecFluxRamp(UI_Handle_t *pHandle,
qd_t Vqd, uint16_t hDurationms) {
MCI_Handle_t *pMCI =
pHandle->pMCI[pHandle->bSelectedDrive];
/* Call MCI Exec Current Ramp */
MCI_ExecFluxRamp(pMCI, Vqd, hDurationms);
return true;
}
__weak void MCI_ExecFluxRamp(MCI_Handle_t *pHandle,
qd_t Iqdref, uint16_t hDurationms) {
pHandle->lastCommand = MCI_EXECFLUXTRAMP;
pHandle->hFinalFlux = Iqdref.d;
pHandle->hDurationms = hDurationms;
pHandle->CommandState =
MCI_COMMAND_NOT_ALREADY_EXECUTED;
}
STC_ExecCurrentRamps
__weak bool STC_ExecCurrentRamps(
SpeednTorqCtrl_Handle_t *pHandle,
int16_t hFinalFlux, uint16_t hDurationms) {
bool AllowedRange = true;
uint32_t wAux;
int32_t wAux1;
int16_t hCurrentReferenceId =
STC_GetFluxRef(pHandle);
if (AllowedRange == true) {
STC_SetControlMode(pHandle, STC_TORQUE_MODE);
if (hDurationms == 0u) {
pHandle->FluxRef = (int32_t)hFinalFlux * 65536;
pHandle->RampRemainingStepId = 0u;
pHandle->IncDecAmountId = 0;
} else {
pHandle->TargetFinalId = hFinalFlux;
wAux = (uint32_t)hDurationms *
(uint32_t)pHandle->STCFrequencyHz;
wAux /= 1000u;
pHandle->RampRemainingStepId = wAux + 1u;
wAux1 = ((int32_t)hFinalFlux -
(int32_t)hCurrentReferenceId) * 65536;
wAux1 /= (int32_t)pHandle->RampRemainingStepId;
pHandle->IncDecAmountId = wAux1;
}
}
return AllowedRange;
}
DEVELOPMENTS

## Slide 16: PI Registers Decoding
The management of the control registers has been refined to allow PI gain tuning (e.g. MC_PROTOCOL_REG_SPEED_KP) directly from CAN, by unpacking the 32-bit wValue variable to set or read both numerator and nominator in a single message.
wValue (32 bit)
16 bit più significativi
16 bit meno significativi
Denominator — Divisor Pow2
(wValue >> 16) & 0xFFFF
→ PID_SetKPDivisorPOW2()
Numerator — Gain Kp
wValue & 0xFFFF
→ PID_SetKP()
Most Significant 16 bits
Least Significant 16 bits
DEVELOPMENTS

## Slide 17: Reading and Writing registers — UI_SetReg / UI_GetReg
Example of SPEED_KP register management: writing the gain and its divisor.
UI_SetReg
__weak bool UI_SetReg(UI_Handle_t *pHandle,
MC_Protocol_REG_t bRegID, int32_t wValue) {
MCI_Handle_t *pMCI =
pHandle->pMCI[pHandle->bSelectedDrive];
MCT_Handle_t *pMCT =
pHandle->pMCT[pHandle->bSelectedDrive];
bool retVal = true;
case MC_PROTOCOL_REG_SPEED_KP: {
uint16_t kp_gain =
(uint16_t)(wValue & 0xFFFF);
uint16_t kp_div_pow2 = (uint16_t)
(((uint32_t)wValue >> 16) & 0xFFFF);
PID_SetKP(pMCT->pPIDSpeed,
(int16_t)kp_gain);
PID_SetKPDivisorPOW2(pMCT->pPIDSpeed,
kp_div_pow2);
} break;
UI_GetReg
__weak int32_t UI_GetReg(UI_Handle_t *pHandle,
MC_Protocol_REG_t bRegID, bool *success) {
MCT_Handle_t *pMCT =
pHandle->pMCT[pHandle->bSelectedDrive];
MCI_Handle_t *pMCI =
pHandle->pMCI[pHandle->bSelectedDrive];
int32_t bRetVal = 0;
case MC_PROTOCOL_REG_SPEED_KP: {
bRetVal =
((int32_t)(PID_GetKPDivisor(pMCT->pPIDSpeed)
& 0xFFFFu) << 16) |
((uint16_t)(PID_GetKP(pMCT->pPIDSpeed)
& 0xFFFFu));
} break;
}
DEVELOPMENTS

## Slide 18: ACK/NACK and GET REG Response Separation
The Issue
The ACK/NACK responses shared the same CAN ID as the GET REG response message, making them indistinguishable.
✓
The two outgoing CAN messages to the DYNO were therefore differentiated by assigning a dedicated identifier based on frame size.
CFCP_TX_IRQ_Handler
__weak void CFCP_TX_IRQ_Handler(
CFCP_Handle_t *pHandle) {
if (FCP_TRANSFER_IDLE != pBaseHandle
->TxFrameState) {
uint8_t tx_data[16];
/* Build the can message to be sent */
TxHeader.Identifier = CAN_TX_MSG_ID_START;
if (pBaseHandle->TxFrame.Size == 4) {
TxHeader.Identifier = 17U;
}
}
}
DEVELOPMENTS

## Slide 19: Validation and Advanced Debugging

## Slide 20: PCAN-View & TRACE32 Debugging
DEBUGGING
The combined use of PCAN-View and TRACE32 allowed dynamic debugging to be performed in real time, from the Dyno to the microcontroller.
1
Frame Injection
(PCAN-USB FD)
Transmission of custom CAN frames with test parameters.
2
FDCAN Interrupt
(Stellar-E)
Instant trigger of IRQ_CAN1_LINE0_HANDLER upon frame arrival.
3
Step-by-Step Execution
(TRACE32)
Breakpoint in DYNO2DWProtocol(): verification of payload unpacking, UI, and Motor Control functions.
4
Bus Response
(0x10 / 0x11)
Real-time validation of the ACK (0xF0) or NACK (0xFF) code, or the response to GET_REG.
DYNO2DW Message Tracking
By sending a packet from PCAN-View (e.g., EXECUTE_COMMAND 0x33 or SET_REG 0x31) and setting breakpoints in TRACE32, it was possible to step through the code line by line in DYNO2DWProtocol to verify that each CAN message correctly mapped to its corresponding DW function.
Flow & Error Analysis
Identified logical execution paths, highlighted redundancies in transmission loops, and visualized PI register IDs for read and write operations.

## Slide 21: PCAN-View Transmit Message List
Test frame configuration used for manual command injection into the microcontroller during debugging.
DEBUGGING

## Slide 22: Hardware setup and basic diagnostics verification
✓
Physical layer & diagnostics (+0x40)
Confirmed via PCAN-View the continuous reception, every 100 ms, of the 10 telemetry packets generated by Send_Status.
✓
ACK/NACK on 0x10 ID and GET REG response on 0x11
Verified that the board responds to each command sent on 0x10 with 0xF0 (ACK) or 0xFF (NACK) or with the desired register value on 0x11.
MCU to Dyno
Qui immagine rx pcan
DEBUGGING

## Slide 23: DW Protocol vs SR5E1 library Discrepancy
Debugging case study uncovering a mismatch between the DW Protocol specification and the SR5E1 library implementation.
1
SET_REG Transmission via PCAN-View
2
DW Specification Message Format
3
Debug Verification of Incorrect SET Handling
!
Conclusion: Byte 0 is not used for payload length, but directly represents the target register ID.
!
DEBUGGING

## Slide 24: DBC file

## Slide 25: What is the .DBC file used for?
DBC FILE
The . DBC (CAN Database) file is the standard configuration file used in the automotive industry to describe the structure of the CAN bus. It acts as a dictionary that translates hexadecimal data into physical signals that can be read by software such as Vector CANalyzer.
The . DBC file defines:
CAN IDs of transmitted and received the messages
Length (DLC) of each message, expressed in bytes
Payload bit position, length, signed/unsigned type, scale factor and offset
Message Tree. DBC
Diagnostics (0x40 – 0x60): 10 periodic telemetry messages.
Motor Controls (0x30+): Registers, Speed/Flux Ramps, and Bitmasks.
MCU Responses: 0x10 (ACK/NACK) and 0x11 (REG_VALUE).
CAN messages

## Slide 26: Examples of Parameters in CAN Messages
EXECUTE_COMMAND (ID 0x33)
SET_RAMP (ID 0x37)
Transmits a bitmask organized on several bytes:
It carries two distinct physical parameters for the speed ramp:
Byte | Bit | Flag
0 | 1 / 2 / 3 | EXE_START_MOTOR / STOP_RAMP / RESET
0 | 5 / 6 / 7 | EXE_PING / FAULT_ACK / ENCODER_ALIGN
1 | 0 / 1 | EXE_IQDREF_CLEAR / GET_BOARD_INFO
Target Speed
Desired final speed (e.g. expressed in RPM)
Duration
Ramp duration, in milliseconds (ms)
EXECUTE_COMMAND signals
SET_RAMP signals
DBC FILE

## Slide 27: Library Alignment — +0x30/+0x40 Offset
The message definition in the .DBC has been updated to closely reflect the architecture of the firmware library.
+0x30/+0x40 Offsets
The commands sent from the Dyno to the inverter maintain the offset convention already used by the library:
0x3B SET_CURRENT_ID
0x3C SET_CURRENT_IQ
New Command Management
For commands not present in the initial library—such as the $I_d$ flux ramp (SET_ID_RAMP)—an unused CAN ID was assigned (avoiding conflicts with existing commands or 0x40+ telemetry) and defined in both the .DBC and the C firmware.
CAN ID Map by Command Range
0x10 – 0x11
MCU Responses
ACK/NACK, REG_VALUE
0x30 – 0x3A
Existing Commands
firmware library
0x3B – 0x3C
New Commands
SET_CURRENT_ID / IQ
NEW
0x40 +
Diagnostics
Periodic telemetry
DBC FILE

## Slide 28: Response messages and structural correction
REG_VALUE — ID 0x11
Response to GET_REG (0x32): The microcontroller transmits the 0x11 ID with the requested register value.
ACK / NACK — ID 0x10
Each command received generates an acknowledgment: 0xF0 = ACK (successful), 0xFF = NACK (error).
Structural correction of the .DBC
BEFORE
0xFF and 0xF0 were incorrectly defined as two distinct CAN IDs.
AFTER
A single unique ID 0x10; 0xF0 and 0xFF become payload values (signals) within the message.
DBC FILE

## Slide 29: CANalyzer & GUI Interface

## Slide 30: Connection architecture: CAN Bus to Python GUI
CANALYZER & GUI
To evolve from manual validation (PCAN-View + TRACE32) to fully automated testing, Vector CANalyzer was integrated: a bridge between the Stellar-E microcontroller and the operator, hiding the hexadecimal register complexity behind a custom Python GUI.
Bus CAN
Stellar-E
CAPL +
file .DBC
Vector
CANalyzer
COM API
win32com.client
GUI
Python
CANalyzer
It handles the timing of the CAN bus, the decoding of the . DBC file, and the execution of CAPL code.
Python
It exclusively manages the user experience and the graphic rendering of the interface.
On startup, Python instantiates Vector.CANalyzer.Application, gaining direct access to the App.SystemVariables namespace.

## Slide 31: CANalyzer
The following shows the Vector CANalyzer interface and the system variable namespace, with which the Python GUI communicates via COM API.
Interfaccia CANalyzer
System Variables
CANALYZER & GUI

## Slide 32: Flow of commands and telemetry
Bus CAN → GUI
GUI → Bus CAN
1
Background capture: Firmware continuously sends the 10 telemetry packets (0x40+) and REG_VALUE response (0x11)
2
Decoding in CANalyzer: CAPL on-message events decode frames via . DBC and update system variables
3
Python reading and rendering: periodic polling via COM API, real-time updating of graphs and indicators
1
Graphical event interception (button/slider) → sysvar writing via COM API
2
CAPL event trigger on sysvar
3
Security Control — Ready Flags for Multi-Parameter Commands: Unlocked Sending Only at Full Flags
4
Assembly according to the . DBC and hardware transmission on the CAN bus
CANALYZER & GUI

## Slide 33: CAPL code
CAPL events observe the system variables written by the GUI and, once the security conditions are met, assemble and transmit the frame on the CAN bus.
// CAPL: COMANDI
on sysvar SET_SPEED_RAMP::SET_RAMP { message SET_RAMP msgSpeedRamp; if (@this == 1 && is_finalSpeed_ready == 1 && is_durSpeed_ready == 1) { msgSpeedRamp.FinalSpeed_execrmp = g_finalSpeed_value; msgSpeedRamp.Duration_execrmp = g_durSpeed_value; output(msgSpeedRamp); } } // SET_REG: void send_pi_message(word reg_id, int val, int denom) { message SET_REG msg; msg.REGISTER_ID = reg_id; msg.REGISTER_VALUE = val; msg.REGISTER_VALUE_DENOM = denom; output(msg); }
// CAPL: DIAGNOSTICA on sysvar SET_SPEED_RAMP::SET_RAMP { on message DIAG_TORQUE_REF
{
@DIAG_MESSAGES::TORQUE_REF = this.DWord(0);
}
on message REG_VALUE
{
@GET_REG::K_num = this.GET_K_NUMERATOR;
@GET_REG::K_den = this.GET_K_DENOMINATOR;
}
CANALYZER & GUI

## Slide 34: Motor Control Panel
CAN Bus: Connection status displayed in the top panel Start Motor / Stop Motor: Motor start and stop commands Temperature / DC Bus Voltage: Real-time DC bus temperature and voltage MC State / Reset Fault: Controller Status and Fault Management
CANALYZER & GUI

## Slide 35: Tab Speed Control
Final Velocity (RPM): Final speed SET
Ramp Duration (ms): Duration of the ramp SET
Apply Speed Ramp: Apply the set values to the Motor
Gauge: shows real-time reference value (REF) and current value (ACT)
CANALYZER & GUI

## Slide 36: PI Controller
Speed / Flux / Torque Regulator: Sections for the three control loops
Kp / Ki: proportional and integral gains of each ring
Num / Den POW2: numerator and denominator (power of 2) of each controller
Set: Apply set values
CANALYZER & GUI

## Slide 37: Tab Current Control
IQ Value (A): Torque-producing current setpoint
ID Value (A): Flux-producing current setpoint
IQ Ramp / ID Ramp: Configurable independent ramps for each current component
Charts: Real-time plot of reference and measured currents over time
CANALYZER & GUI

## Slide 38: Tab Live Charts
Speed Overview: Real-time speed gauge
IQ - Torque Current: Torque Current Graph
ID - Flux Current: Flux current graph
CANALYZER & GUI

## Slide 39: Conclusions and results
CONCLUSIONS
✓
CAN Library Validated
Resolved critical issues in ID mapping and registers decoding.
✓
New features
Independent I_d/I_q control, flux ramp, PI tuning via CAN.
✓
DBC Refactored
Messages aligned to the library, correct ACK/NACK responses.
✓
GUI Development
Python GUI + Vector CANalyzer for complete real-time testing.

## Slide 40
Find out more at www.st.com

## Slide 41
For further support in creating a PowerPoint presentation, including graphic assets, formatting tools and additional information on the ST brand
you can visit the ST Brand Portal https://brandportal.st.com